## Slide 1: Video Transcoding for Mobile Telephony
M. Bonuccelli
F. Martelli
L. D’Amaro

## Slide 2: Overview
Motivations
Video Coding
Video Transcoding
Future work

## Slide 3: Motivations
In the 3rd generation mobile telephony, many complex applications are foreseen
  Video on demand
  Video telephony
  Web browsing
  …

## Slide 4: Quality of service classes
Conversational (bidirectional)
Streaming (one way)
Interactive (e.g. web browsing)
Background (e.g. email, ftp)
Delay sensitive
Delay insensitive
Streaming (one way)

## Slide 5: 3G System feature
Handoff: a user moves from one cell to a neighboring one when involved in a call
The user needs a channel in the new cell:
  If available, he gets it
  If not available, subrating is performed
Subrating: temporary division of an occupied full rate channel into two half rate channels

## Slide 6: Video streaming problem
When a channel bandwidth is halved, a buffer underflow may occur
In that case the video sequence stops (still frame) in the receiving terminal
To avoid this problem it is needed to code the video sequence with a lower bit rate (video transcoding)

## Slide 7: Video Coding
A video sequence is recursively split:

## Slide 8: Video Compression
Most coding video standards are based on the same hybrid framework (DCT/MCP)
  Intraframe coding: spatial redundancy within a frame is removed by DCT (Discrete Cosine Transform)
  Interframe coding: temporal redundancy among frames is removed by MCP (Motion Compensated Prediction)

## Slide 9: Intraframe Coding
It consists of the following steps:
  DCT
  Quantization
  Entropic coding:
    Zig-Zag Scan
    Run Length Coding
    Variable Length Coding

## Slide 10: Interframe Coding
It consists of coding only the differences with a reference frame:
  Motion Vector: indicates the reference frame area most similar to the macroblock to code
  Prediction Errors: the differences between the best match area and the macroblock are coded in the same manner of the intraframe coding

## Slide 11: Image Coding Types
There are three frame types:
  I-frames (intra-frames)
  P-frames (forward predicted frames)
  B-frames (bi-directional predicted frames)

## Slide 12: Motion Estimation
It searches the best match of a macroblock in the reference frame within a search region
The best match is that one having the minimum SAD (Sum of Absolute Differences) value

## Slide 13: Motion Estimation Algorithm
The Full Search algorithm computes the SAD values of all possible matching areas in the search region
It is the most computational complex motion estimation algorithm (it requires about 60-70% of video compression total time)

## Slide 14: Fast Motion Estimation Algorithms
Many algorithms of fast ME have been proposed to reduce the complexity of Full Search
They significantly reduce the number of reference frame areas to test
  3 step search
  PMVFAST (Predictive Motion Vector Field Adaptive Search Technique)
  APDZS (Advanced Predictive Diamond Zonal search)
  …

## Slide 15: Rate Control
By using fixed quantization parameters, the compressed video sequence has a variable bit rate; this may cause buffer underflow or overflow
The rate control concerns about the computation of quantization parameters in order to adapt the video streaming bit rate with the channel bandwidth
It computes the complexity estimation of the current frame by using that one of previous frame

## Slide 16: Standard DCT/MCP Video Codec

## Slide 17: Video Transcoding
It is a process in which a compressed video is converted in another one with:
  Different format
  Different frame resolution (spatial transcoding)
  Different frame rate (temporal transcoding)
  Different video quality (bit rate transcoding)
Differently from a conventional video encoder, a video transcoder takes as input a compressed video stream from which it can extract parameters and statistics to encode the output video stream, without recomputing them

## Slide 18: Spatial Transcoding
It consists of reducing the frame resolution of the input video stream
There are two types of spatial transconding:
  Subsampling 2:1
  Arbitrary sampling
In both approaches it is necessary to recompute the motion vectors and the prediction errors by combining and scaling the original ones

## Slide 19: Temporal Transcoding
It consists of dropping some frames, then it is needed to recompute the motion vectors not still valid (because they point to discarded frames)
The new motion vectors can be obtained by interpolating the motion vectors of all dropped frames between the current frame and the last not dropped frame
The prediction errors must be computed according to the new motion vector

## Slide 20: Bit-Rate Transcoding
It consists of decreasing the video stream bit rate by reducing the video quality without changing the frame rate or the frame resolution
It can be performed by a specific Rate Control function, where the complexity of the current frame, instead of being estimated, can be directly extracted from the input video

## Slide 21: Video Transcoding Architectures
There are essentially three types of video transcoding architectures:
  Pixel Domain Transcoder
  DCT Domain Transcoder
  Open-Loop Transcoder

## Slide 22: Cascaded Pixel Domain Transcoder

## Slide 23: Fast Pixel Domain Transcoder

## Slide 24: DCT Domain Transcoder

## Slide 25: Open-Loop Transcoder

## Slide 26: Future Work
Investigate the video transcoding problem caused by subrating
Propose new algorithmic and/or architectural solutions