## Slide 1
Design for a centralized
Path Computation System
Giodi Giorgi
(g.giorgi@iet.unipi.it)
Università degli Studi di Pisa
Dipartimento di Ingegneria della Informazione: Elettronica, Informatica, Telecomunicazioni
Gruppo di Ricerca in Reti di Telecomunicazioni
http:// wwwtlc.iet.unipi.it

## Slide 2: Summary
some results of an intensive testing campaign
conclusions and future work.
the implementation of a centralized Path Computation System (PCS) suited for transport networks with a GMPLS control plane
the design issues for the proposed implementation, with particular emphasis on the centralized approach and on the strategies for achieving the connection survivability
the requirements for the PCS in a centralized GMPLS network scenario
the performances of bandwidth-dependent TE metrics and the effects of different TE functions on the load balancing

## Slide 3: Introduction
GMPLS architecture is based on:
The standardization committees (e.g. ITU-T, OIF and IETF) are all converging in the design of an integrated network with a common GMPLS control plane.
GMPLS will manage all the network data planes, providing
From a routing perspective, the GMPLS extensions
  the required automation in the computation;
  the setup and the recovery of circuits for next-generation OTN.
  a set of extensions to protocols for routing (e.g. OSPF and IS-IS) and signalling (e.g. RSVP), just available in IP networks;
  a new link management protocol (i.e. LMP), designed from scratch in order to handle correctly the distinction between the data plane and the control plane.
  provide new information for circuit computation;
  enable configurable TE policies and new recovery strategies.

## Slide 4: GMPLS network model with a centralized PCS
NM
GMPLS
NE
TE Topology
GMPLS
NE
GMPLS
NE
GMPLS
NE
GMPLS
NE
NM Network Manager
NE Network Element
Worker route computation
Backup route computation
Worker LSP
Backup LSP
Manager-to-NE comms
GMPLS Signaling
The architectural choice is for the implementation of the PCS module inside a centralized network manager (NM).
PCS acts as a path computation server receiving from the NE the topology information and the computation requests across a single/multi-area/AS.
The LSPs are communicated to the ingress NE, triggering a standard signalling session.
This solution promises to be the most effective for a full and flexible handling of:
TE
particularly when these requirements need to be extended to a multi-area (or multi-domain) scenario.
survivability into the network

## Slide 5: Requirements for a GMPLS PCS
standard SPF algorithms are not suited, they cumulate only the link metric:
  a modified SPF algorithm (CSPF) is needed, because the routes should be the shortest among those which satisfy the required set of constraints.
A GMPLS path calculator is expected to return LSPs which try to match some constraints derived from the TE information.
For routing purposes, to transform the traditional links in TE-links, a set of properties is assigned to each link:
PCS for standard IP networks are generally based on:
Traffic Engineering is fundamental
  to optimize network performances
  for load balancing in the transport network, in order to avoid the overloading (up to saturation) of some network resources and the sub-utilization of others (TE Resource Oriented)
  SRLG list,
  inherent protections.
  TE metric,
  available/used bandwidths,
  resource colours,
  distributed, fast and simple routing algorithms (e.g. of the SPF),
  this algorithms walk along a graph derived from the real network.

## Slide 6: Connection survivability
  It depends on the recovery strategy implemented in the network.
  New recovery strategies are enabled by the GMPLS control plane.
RECOVERY
PATH-LEVEL
SPAN-LEVEL
PROTECTION
1+1
M:N (1:N, 1:1)
PROTECTION
1+1
M:N (1:N, 1:1)
RESTORATION
re-computation
pre-panne Fast Restoration
RESTORATION
re-computation
pre-planned Fast Restoration
a failure notification is propagated till the end nodes of the affected LSP and there solved (a.k.a end-to-end)
a failure is notified and solved at intermediate nodes, next to the failed resource (a.k.a. local repair)
perform pre-calculation and pre-allocation of a backup LSP or set of spans
a new LSP is dynamically allocated only at time of failure (On-the-fly) or it is pre-computed and only booked for a future restoration (Fast Restoration)

## Slide 7: Connection survivability
Restoration
span level strategies
sub-optimality
waste of resources in the network
optimality
more efficient, best end-to-end backup path
path level strategies
in case of a fault, a higher blocking probability for the restoring traffic might be experimented
fits better the dynamical assignment/release of the network resources
failure handling by control plane mechanisms instead of hardware ones (e.g. detection, notification and mitigation).

## Slide 8: Disjointness
A common requirement for all the recovery strategies
In the GMPLS architecture different levels of disjointness for LSPs are defined:
related to the logical layer of the transport network (TE-topology)
related to the physical layer, as SRLGs may be used to locate conduits, fibres or general risks for physical resources.
Bhandari
Two-Step-Approach
Node
Link
SRLG
}
This is needed to minimize the blocking probability of the dynamical recovery action in case of fault.
easy to be implemented,
limited complexity both of the SPF and of the network transformation,
lower guarantee to find the completely disjoint pair of paths.
higher complexity due to a modified SPF running on a negative graphs and to an interlacing procedure,
able to calculate the optimum pair of disjoint paths with lowest cost.

## Slide 9: TSA algorithm
Run Dijkstra between source and destination vertices
Network Graph
Each link incident on any node of the first shortest path (except for the endpoint nodes) is transformed adding an extra cost.
2 vertex disjoint paths
Run Dijkstra between source and destination vertices
START

## Slide 10: Example of TSA algorithm
A
E
B
G
C
D
Z
F
1
1
1
1
1
2
7
3
4
3
8
1
3
ExtraCost = 100 > 36
Primary path cost = 4
Secondary path cost = 11
103
101
103
101
101
101
101
102

## Slide 11: Bhandari’s algorithm
Run modified Dijkstra between source and destination vertices
Network Graph
Split incident edge in the two component arcs, terminating one on the first sub-vertex and the other on the latter one.
Split each vertex on the shortest path in two sub-vertices connected by an arc of length 0 directed towards source and by an arc of length l directed towards destination.
Replace edges of the shortest path with two single arcs, the first one directed towards source vertex with the negative cost and the second one directed towards destination vertex adding an extra cost a
Coalesce sub-vertices and remove zero length arcs.
Erase interlaced edges
2 vertex disjoint paths
Run modified Dijkstra between source and destination vertices

## Slide 12: Example of Bhandari’s algorithm
A
E
B
G
C
D
Z
F
1
1
1
1
1
2
7
3
4
3
8
1
3
l = 100 > 36
a = 700
BI
DI
DII
CII
CI
BII
a+1
a+1
a+1
a+1
l
l
l
-1
-1
-1
-1
0
0
0
2
3
1
3

## Slide 13: Example of Bhandari’s algorithm
l = 100 > 36
a = 700
Primary path cost = 5
Secondary path cost = 8
A
E
B
G
C
D
Z
F
1
1
1
1
1
2
7
3
4
3
8
1
3
1

## Slide 14: TSA v.s. Bhandari’s
In spite of available resources, TSA algorithm does not always find the two completely disjoint paths
TSA algorithm fails the research of the two disjoint paths, whereas Bhandari’s algrithm achieves two completely disjoint paths

## Slide 15: Class of Recovery - CoR
Gold:
Silver:
Bronze:
Unprotected:
  lowest blocking probability for the recovery
  fastest reaction times (e.g. around 50ms)
  this CoR applies to the Protection strategies
  it implies the computation of a pair of maximally disjoint paths to guarantee the total resource redundancy and uncorrelation.
  fast reaction times (e.g. less than 1s)
  this CoR applies to Fast Restoration strategies
  it implies the computation of a pair of disjoint paths in order to guarantee a level of resource uncorrelation.
  when reaction times around 1s are acceptable
  this CoR applies to On-the-fly Restoration strategies
  it implies the computation of an optimal worker path when the request is received and the computation of an optimal backup one at failure occurrence.
  no survivability is requested for the traffic of the LSP (e.g. preemptable or BE traffic).

## Slide 16: Class of Recovery - CoR
Gold service:
Silver service:
Bronze service:
  is the most exacting in terms of optimality of the computation,
  a least cost pair of disjoint paths is required, providing that it is also the maximally disjoint pair in the network.
  among many algorithms proposed, the Bhandari’s one promises lower theoretical complexity.
  is sub-optimal, because the backup paths do not take into account any modification of the network load occurred in the meanwhile.
  we compute the backup LSP trying to satisfy the required disjointness, but with no guarantee for success and for optimality (i.e. the resulting backup not maximally disjoint and the pair might not have the cumulative shortest cost in the network).
  for this kind of computation we used the TSA algorithm
  is the slowest approach, because of the time spent for failure detection, localisation, notification and mitigation.

## Slide 17: Network topologies
1
2
N
2N
MN
1
2
N
2N
MN
1
2
N
2N
MN
Manhattan topology
Meshed-Manhattan topology
Half-meshed-Manhattan topology
Interconnected rings topology
64 nodes, MD = 3.14
Nodes: 49 - 100
MD = 3,43 - 3,60
Nodes: 16, 25, 36, 49, 64, 100
MD = 4,1 4,5 4,7 4,9 5,0 5,2
Nodes: 16, 25, 36, 49, 64, 100
MD = 5,2 5,8 6,1 6,4 6,6 6,8
Measures have been collected on different topologies with increasing meshing degrees:

## Slide 18: Simulation environment
All these topologies have been modelled with:
Algorithm’s effectiveness in creating maximally disjoint paths
Algorithm’s effectiveness in computing valid paths
  generic nodes
  the number of computed LSPs (comp_path);
  the number of totally link-/node-disjoint pairs of LSPs (disjoint);
  the mean computation time for each LSP request (time).
  connected by a TE-link with random values for its TE-information
  TE-links
  assumed to be bi-directional, each configured with 4 STM-64 ports VC4-multiplexed
A large number of LSP computations (req_path) have been requested on each topology, trying to establish a stress condition.
We defined a Global Performance Factor (GPF) as:
For each topology have been observed:

## Slide 19: Global Performance Factor
Alignment when meshing degree increases (higher resource availability).
Trend strictly related to the variance of the TE-metric values for the TE-links
The higher number of path computation failures at lower meshing degrees is strictly related to the resource availability on TE-links.
In case of TSA, this merges with the intrinsic sub-optimality of this algorithm.
 | Link Disjoint | Node Disjoint
Mean higher performance B v.s. TSA | +0.57% | +2.79%

## Slide 20: Mean Computation Time
 | Link | Node
increase in MCT for each LSP request | +3.59% | +4.14%

## Slide 21: Theoretical infinite resources

## Slide 22: BW-Dependent TE metrics
The routing engine inside our PCS module is based on Dijkstra SPF algorithm.
In order to handle Constrained SPF computations, we added a TE-constraints validation step.
For example the check on the bandwidth availability of the candidate link.
In order to let the algorithm converge towards an optimal SPF solution (e.g. between those which satisfies the required TE-constraints), we choose a bandwidth-dependent metric:

## Slide 23: TE policy functions
K = resource cost per unit
where:
t = smoothing factor
These policy functions increase the total cost of the link as allocated bandwidth increases, so as to avoid the overloading of the link and the resulting network congestion.

## Slide 24: TE policy functions
policy2 achieves a better flexibility in increasing the cost of the TE-link
policy1 discourages the link picking as the allocated bandwidth increases on it
K = 2, t = 1.5, BWthr = 75% of BWtot

## Slide 25: Policy2

## Slide 26: Simulation environment
All the requests, with recovery requirements, have been configured with four possible values for the bandwidth:
  VC4 (e.g. 95.5% of req_path at 139 Mbit/s ca.);
For each topology have been observed:
  the number of computed LSPs (comp_path);
  VC4-4c (e.g. 3.0% of req_path at 556 Mbit/s ca.);
  VC4-16c (e.g. 1.0% of req_path at 2224 Mbit/s ca.);
  VC4-64c (e.g. 0.5% of req_path at 8896 Mbit/s ca.).
  the mean TE-link usage in % (link_utilization);
  the number of totally disjoint pairs of LSPs (disjoint).

## Slide 27: Link utilization
higher link utilization achieved when policies are used;
greater improvements are obtainable for lower meshing degree;
improvement in the fairer utilization of the network resources.

## Slide 28: GPF with different TE policies
Computations with TE policies achieve:
mean higher performance both for Gold and for Silver CoRs,
an improvement in the fairer utilization of the network resources.
These advantages are much evident in case of Silver CoR, because of the worst resource picking due to the sub-optimality of algorithm adopted.

## Slide 29: Conclusion
GPF | Silver CoR | Gold CoR
policy_1 vs. no_policy | +2.86% | +5.28%
policy_2 vs. no_policy | +2.49% | +4.01%
Link Util. | Bronze CoR | Silver CoR | Gold CoR
policy_1 vs. no_policy | +2.66% | +0.76% | +1.75%
policy_2 vs. no_policy | +2.75% | +0.80% | +2.01%
The advantages of defining complex policy functions (policy_1) do not pay for the introduced CPU complexity
policy2 improves policy1 performance for less than 0.25%
it worsens policy1 performance in case of GPF
A simple policy function (policy1) is suitable and effective for a good trade-off between the computational load on CPU and the achievable performance in terms of:
load balancing
blocking probability

## Slide 30: Future work
PDP
COPS-MAID
PEP
Neighb. BBs
Host1
MA-BR1
CR2
CR3
MA-BR2
CR1
Host2
AAA
DNM
SNMP
OSPF-TE
TC
RM
X IWU
LSP IWU
RSVP-TE
OSPF-TE
SNMP
AC Admission Control
AAA Accounting,Authoriz.,Authent.
BB Bandwidth Broker
DNM Domain Network Manager
IWU Inter-Working Unit
PCS Path Computation System
PDP Policy Decision Point
PEP Policy Enforcement Point
RM Router Manager
TC Traffic Control
SNMP
BB
AC/PCS
OSPF-TE

## Slide 31: Future work
BB Adjacent Domains’ SLAs database
(BB-ADS- DB)
Domain Network Manager
(DNM)
COPS
Server
to/from
MA-BR
Inter-Domain Communication Module (IDCM)
BB LSP Policy database
(BB-LSP-P- DB)
Policy Database
(P-DB)
Command Line Interface (CLI)
Policy Engine (PE)
to/from
neighb. BB
BB
Stats Collection Module
(BB SCM)
BB Installed LSP database
(BB-LSP-DB)
SNMP API
to/from
BR/CR/
MA-BR
BB Network Database
(BB-Net-DB)
Zebra OSPF-TE
daemons
AC & Path Computation System
(PCS)
to/from
BR/CR/
MA-BR

## Slide 32: Future work
Topology Loader
Network DB
PCS
Path Requester
I/F 92
Internal
API
I/F 91
a
a
b
b