## Slide 1: Integrating Wireless Wireline and Internet Networks JAIN MAP API
Maurizio Bonuccelli
Francesca Martelli
Piero Lauri
Renata Bandelloni
Rita Arrighi
Francesca Lonetti

## Slide 2: JAIN
Java APIs for Integrated Networks
JAIN provides a set of Java APIs focused on emerging network protocols and architectures driven by convergence of traditional telecommunication and IP networks
Two levels:
  Application Level
  Protocol Level

## Slide 3: MAP
Mobile Application Part
Protocol used by entities beloning to mobile network infrastructure, not by mobile terminals
MAP handles numerous services about mobility

## Slide 4: JAIN MAP API
The JAIN MAP API Specification defines APIs which allow for the rapid creation and deployment of dynamic telephony services into a Java platform
The API specified by JAIN Community are based on the ETSI MAP GSM and IS41 specifications.
JAIN MAP API specification gives a functional definition indipendent from the protocols stack below

## Slide 5: Most interesting services
Sending/receiving short messages to/from mobile telephones (Transaction capability)
Exchange of service specific data between the mobile telephone and a service application in the mobile network (Session capability)
Retrieval of information about mobile telephones, such as position/location (Position capability)
Retrieval of information about mobile telephones, such as availability/status (Information capability)

## Slide 6: JAIN MAP API Specification
For each capability:
JainListener interface;
JainProvider interface;
Stack interface;
Factory class;
Java Event class for each primitive;
Parameter classes;
Exception classes.
Notes: Le specifiche della JAIN MAP API definiscono una struttura ad oggetti composta principalmente dalle seguenti parti:
JainListener interface che deve essere implementata dall’applicazione del JAIN MAP API User, per la funzionalità che vuole usare;
JainProvider interface;, la cui implementazione è compito di chi realizza la particolare funzionalità della JAIN MAP API. Ci sarà un’istanza di un oggetto provider per ogni dominio di servizio, che denota un gruppo di abbonati per una specifica funzionalità, ed è caratterizzato da diversi parametri, tra cui la funzionalità supportata, lo stack che usa, il range degli indirizzi degli abbonati, ecc. Potranno quindi esistere più oggetti provider per ogni funzionalità;
Stack, interface; che deve essere implementata sempre dagli sviluppatori della JAIN MAP API. È la rappresentazione dello stack nel sistema, che può essere usato dalla JAIN MAP API, e funge da factory per gli oggetti provider;
Factory class;utilizzata per istanziare gli oggetti stack;
Java Event classper ogni primitiva;
· una classe che rappresenta il parametro di una primitiva con una struttura complessa, che quindi non può essere rappresentato da un tipo base di Java;
una classe che rappresenta il parametro di una primitiva con una struttura complessa, che quindi non può essere rappresentato da un tipo base di Java;
Exception classes per ogni eccezione, con cui viene segnalato all'applicazione il verificarsi di un errore nella JAIN MAP API.

## Slide 7: JAIN MAP API Implementation
For each capability, we added the following classes in its packet:
  OutgoingThread
  IncomingThread (if necessary)
  Various specific classes
And
  JainMapUserForCAPABILITY (to test APIs)

## Slide 8: MAP Protocol
Because we haven’t a real MAP protocol, we simulated it
A packet for each MAP capability
A dialogue for each session
MapProvider, MapListener, MapEvent, MapException
Windows to simulate Map Answers

## Slide 9: MAP Version
The used ETSI standard version is
  Digital cellular telecommunications system (Phase 2+); Mobile Application Part (MAP) specification (GSM 09.02 version 7.1.0 Release 1998)
Except for LCS Capability, for which we have used
  Digital cellular telecommunications system (Phase 2+) (GSM); Universal Mobile Telecommunications System (UMTS); Mobile Application Part (MAP) specification (3GPP TS 29.002 version 4.5.0 Release 4)

## Slide 10: Outgoing Session Framework
J
A
I
N
M
A
P
U
S
E
R
M
A
P
E
N
T
I
T
Y

## Slide 11: Incoming Session Framework
J
A
I
N
M
A
P
U
S
E
R
M
A
P
E
N
T
I
T
Y

## Slide 12: JAIN MAP API Transaction Capability
Implemented by Renata Bandelloni, Francesca Martelli
Based on SMS service
JAIN MAP APIs for this service reside on Service Centre, which interface itself both with HLR and MSC

## Slide 13: JAIN MAP API Session Capability
Implemented by Rita Arrighi, Francesca Martelli
Based on USSD service, which is a transport mechanism that is used to transport data for Operator Specific Services between the MS and the network.
USSD is an important mechanism to support such services even when roaming outside the home-PLMN.
The functional entity where USSD-handler reside is gsmSCF.
JAIN MAP API interface reside in HLR or in gsmSCF

## Slide 14: GSM Network

## Slide 15: JAIN MAP API Position Capability
Implemented by Francesca Martelli
The Location Service (LCS) has recently been introduced in ETSI MAP.
Functional entities are:
  LCS client: it may be internal or external to the PLMN.
  GMLC - Gateway Mobile Location Center. Provides access to location service for LCS clients (internal or external). JAIN MAP API interface reside here
  SMLC - Serving Mobile Location Center: it is a database and processing entity that manages the procedures for obtaining the geographic location of a target MS. The SMLC manages a set of LMUs in its coverage area.
  LMU - Location Measurement Unit. The LMU performs location measurements in the visited PLMN.
Conceptually similar to Transaction Capability

## Slide 16: JAIN MAP API Information Capability
Implemented by Francesca Martelli
The gsmSCF interrogates HLR for information about a particular subscriber, for which it is entitled to do so. This may be information about subscriber state and/or location information
The MAP operation Any-Time-Interrogation (ATI) is used by the gsmSCF to do such an interrogation to the HLR
Support for the Any-Time-Interrogation operation is a network operator option
JAIN MAP API interface reside on gsmSCF

## Slide 17: Conclusions and future work
All JAIN MAP APIs for ETSI MAP GSM are implemented
A UML model is given
Two new services are created
APIs can be extended for UMTS technology
Other new services can be created