## Slide 1: New Service on JAIN MAP
Rita Arrighi

## Slide 2: USSD Service: Unstructured Supplementary Service Data
Used by MS and network applications: the goal is to exchange information or commands
Used to invoke supplementary services or to implement non-standardized services
It is session-oriented: not store-and-forward, so more quick

## Slide 3: USSD service
Network initiated: e.g. credit notification
Mobile initiated: request for informations. In this case, there is a standard format:
Application corresponding to SC (can be in MSC, VLR, HLR) is started
START | SC | * | SIa | * | SIb | * | SIc | #

## Slide 4: MAP services related to USSD
5
6
4
3
1
MS
MSC
VLR
HLR
gsmSCF
ProcessUnstructuredSSRequest
UnstructuredSSRequest
UnstructuredSSRequestResult
ProcessUnstructuredSSRequestResult
UnstructuredSSNotify
UnstructuredSSNotifyResult
Mobile
Initiated
Network
Initiated
2

## Slide 5: JAIN MAP services related to USSD
5
6
4
3
2
1
MS
MSC
VLR
HLR
gsmSCF
ProcessUnstructuredSSRequest
UnstructuredSSRequest
UnstructuredSSRequestResult
ProcessUnstructuredSSRequestResult
UnstructuredSSNotify
UnstructuredSSNotifyResult
Mobile
Initiated
Network
Initiated
SessionOpenInd
SessionDataReq
SessionOpenReq
SessionDataInd
SessionCloseReq
7
SessionDataInd
SessionCloseReq

## Slide 6: Objectives of new service
New service as a bridge between Internet and GSM network
It can be used by any GSM user
It uses the Message Session Capability of JAIN MAP API
It shows the simple use of JAIN MAP API
There is not in actual market

## Slide 7: The new service
Any GSM user can know if there is a new e-mail on a specified mail_server
Application run on gsmSCF entity, belonging to GSM network, but connected to Internet
IMAP or POP protocol can be used to connect with the mailserver

## Slide 8: Application Framework
Default_listener receives Jain primitives SessionOpenInd+ SessionDataInd,
USSD string format is:
*133*mailserver*user*password#
Default_listener, by service code, instances a handler listener
Connection with the Mail Server: IMAP or POP
Connection
With IMAP
USSD string
parsing
IMAP Mail Server interrogation
POP Mail Server interrogation
No Response from Mail Server
JAIN Response
Connection
With POP
accepted
accepted
refused
refused
Notes: IMAP: più pratico per noi, ma meno diffuso
POP: più usato, ma non risponde esattamente alle nostre esigenze (necessaria analisi dell’header delle mail)

## Slide 9: Conclusion and future work
A new service integrating GSM and internet networks was created
Improvements can be:
  Password encrypted
  e-mail from specified address
  …