## Slide 1: Workshop Pisatel 2002 Soluzioni di co-decodifica audio/video Pisa, 12 Dicembre 2002

## Slide 2: Background
The new (3G+) services will more and more require integration of:
Text
Voice/audio
Video
Natural and synthetic elements
Full interaction with end-user

## Slide 3: Background
Typical example of such services are:
Multimedia conference (Netmeeting +  virtual reality)
Gaming
Augmented reality
Remote teaching
...
One of the key factors for the success of the future multimedia systems is the possibility to implement such services on terminals and network elements.

## Slide 4: Issues to be solved
MPEG4 is a solution to provide such services but ...
The computational complexity to encode/decode or to perform trans-coding is high (impact on computational power and delay)
Real time applications are delay sensitive
Trade off between processing performance and processing time
A high power efficiency is required especially in the terminal
and last but not least ... costs need to be kept low

## Slide 5: Computational complexity with MPEG4
In particular the most demanding operations are:
Motion estimation, i. e. block matching techniques. If more blocks are looked for, the better the compression (but the longer the time it takes)=>Trade-offs needed
Motion compensation
Discrete Cosine Transform (a 2D-Fourier transform)
The above operations are particularly resource demanding if blocks are small and/or arbitrarily shaped (especially when the shape has great changes)

## Slide 6: Pre-processing and channel coding
Channel coding (how suitably protect data against losses ? Information carried by packets have different importance and information content)
Object segmentation : MPEG4 greatest innovation relies on the possibility of objects coding, which can be accomplished after shape detection (for instance a face), which is one more time consuming task.

## Slide 7: Activity Goals
1 - Investigate the performance of state of art processors (e.g. latest DSP) in order to determine what functionalities/profiles can be implemented in terminals and network elements
2 – Realize a prototype of video coder MPE4-based, which possibly integrate the shape detection
3 – Performance evaluation in comparison with hardware-based solution (e.g. ASIC).