Titolo
VII. System Specification (I)

---
Objectives
To discuss the importance of models for the definition of specifications
To show formalisms that can be used to define system models
To discuss properties and compare such formalisms
To provide examples

---
Topics
To distinguish among formal and informal specifications
Operational vs. Descriptive Models
Introduce some operational model:
  - Data Flow Diagrams (DFD)
  - Finite State Machines (FSM)
  - Petri Nets (PN)
The material that will be discussed today and tomorrow is covered by [GJM] Chapter 5 and/or [Som] Chapters 8,10

---
How to increase Specification Qualities
Spec should be: Clear, Unambiguous, Understandable
Should not be: Contradictory or Inconsistent, Incomplete
Models are description of the system abstracting away unimportant details, so to make the system “tractable”
Formal specifications vs. Informal specifications
  - Use of formalisms make spec precise and augment automatic verification possibilities
  - Informal spec more flexible, leave more decision space to the implementer
Semiformal often we use notation which semantics has not been defined so precisely (e.g. UML)

---
Formal Spec and Verification
Formal specs are a powerful tool for making easier many development phases in particular for analysis and verification purpose
Just some keyword:
  - Model Checking
  - Model Based Testing
  - Simulation and prototyping

---
Operational vs. Descriptive Specification
Operational specification describe the system in term of the expected behaviour generally providing a model
Descriptive specifications describe the system in term of desired properties for the system
An example from mathematics:
  - Take a string of length “r” and fix at one of its extreme a pencil. Then fix the other extreme to a sheet using a pin. Now tightening the string move the pencil over the sheet describing a circle.
  - x 2 + y 2 = r 2
  - which one is a descriptive or an operational specification?

---
Operational Specifications – DFD
Data Flow Diagrams:
  - Used to specify functions of a system and how data flow from functions to functions
Systems are seen as collections of functions that manipulate data
  - Data can be stored in repositories
  - Data can flow
  - Data can be transferred from and to the external environment

---
DFD – graphical notation
Example – a simple
arithmetical function:
  - (a+b)*(a+c*d)

---
DFD – a supermarket example (I)

---
DFD – a supermarket example (II)
The functionality “gestione acquisti cliente” is certainly a macro activity that could be split
In case of supermarket wants to apply discounts for some products, in a certain period, to some clients, how these information could be introduced in the system?

---
DFD Characteristics
DFD is certainly a semi-formal notation
Lack of precise semantics:
  - Function definition can be defined more precisely using more formal description
No concept of control in such kind of diagrams
  - Diagrams do not specify how data are used and output are produced
Synchronization between functions is not specified

---
How to overcome DFD weakness
Use of complementary notation to express those aspects that are not adequately described by DFD
Augment the DFD introducing mechanisms that allow to express the missing aspects
Revise the traditional definition of DFD to make it fully formal

---
Operational Specifications – FSM
A Finite State Machine (FSM) is an abstract automaton that permits to describe the control flow of a system
Mathematically FSM are defined by:
  - A finite set of states Q
  - A finite set of input I
  - A transition function δ: Q x I --> Q
A simple switch can be described by the following FSM:
  - Q = [On, Off]
  - I = [Switch]
  - δ = [ (On,Switch) --> Off,
            (Off,Switch) --> On]

---
FSM graphical representation
A simple example of an
electrical equipment including
a safety mechanism:

---
FSM with Input and Output
A Finite State Machine (FSM) extension permits to distinguish among input and output data
Mathematically I/O FSM are defined by:
  - A finite set of states Q
  - A finite set of input I
  - A finite set of output O
  - A transition function δ: Q x I --> Q x O
How FSM can be composed originating a system FSM?
  - Resulting machine have a number of state given by the product of the number of states for each composing machine
  - We take a simple (and a bit simplicistic) approach

---
FSM – Thinking Philosophers (I)

---
FSM – Thinking Philosophers (I)

---
FSM and continuous systems
FSM can store a finite quantity of information (Finite-memory devices)
FSM can be cumbersome to describe even “finite” systems requiring to formally express details that sometimes are easier to understand using natural language
In practice computer always have a finite memory but number of states is unmanageably large.
How to manage these situations:
  - Ignore details
  - Complement diagrams with natural language comments
  - Change model (LTS, PN, ...)
  - Enrich FSM (i.e. Introduce a language to annotate transitions)

---
FSM for a Producer/Consumer System

---
Deriving the Parallel Machine

---
The Buffered Producer/Consumer System

---
FSM limitations
Composing machines the number of states raise drastically
We could leave the FSM are they are defined for the subsystems and use composition rules.
Still some problem persist
  - The system must be always in a unique state and can perform only one action at any instant of time
FSM permit to express only synchronous interactions
  - Not really adequate to describe general concurrent systems

---
FSM Exercises
FSM for a two switch lighting systems
Two lamps and one button
  - Different alternatives to model the same system

---
Key points
On today lesson we introduced and discussed:
  - Models to describe software systems have been introduce
  - Properties that permit to classify different modelling language
    - Operational vs. Descriptive
    - Formal vs. Semiformal vs. Informal
  - Data Flow Diagram (DFD)
  - Finite State Machine (FSM)